## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.10
Lecture 20 – November 29, 2022
Aarch32 Assembly – Part 5
Frontier Exascale

## Slide 2: push: Multiple Register Save (str to stack)
push copies the contents of the {reg list} to stack segment memory
push Also subtracts (# of registers saved) * (4 bytes) from the sp to allocate space on the stack
  sp = sp – (# registers_saved * 4)
this must always be true: sp % 8 == 0
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
save registers
push{r4-r6, r8, fp, lr}
r8
r4
r5
lr
fp
r6
CPU registers to Save
copy
Registers are pushed on to the stack in order
right (high memory) to left (low memory)
If you have no stack variables (later) then always push an EVEN number of registers!
sp after push
allocated space
(# registers) * (4 bytes)
stack segment low memory
stack segment high memory
x
sp before push

## Slide 3: pop: Multiple Register Restore (ldr from stack)
pop copies the contents of stack segment memory to the {reg list}
pop adds: (# of registers restored) * (4 bytes) to sp to deallocate space on the stack
  sp = sp + (# registers restored * 4)
Remember: {reg list} must be the same in both the push and the corresponding pop
stack segment high memory
r8
r4
r5
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
lr
fp
r6
stack segment low memory
CPU registers
copy
Restored register contents
Registers are pop’d from the stack in order
left (low memory) to right (high memory)
restore registers
pop{r4-r6,r8,fp,lr}
sp after pop
deallocated space
(# registers) * (4 bytes)
x
sp before pop

## Slide 4: Local Variables are Part of Each Stack Frame
Local variables are on the stack below the lowest numbered saved (pushed) register
#define BFSZ 4
int main(void)
{
char buf[BFSZ]; // BFSZ bytes
...
sp
saved lr
saved fp
buf[BFSZ]
BFSZ
buf[0]
buf[BFSZ-1]
x
saved register
saved register
sp
saved lr
saved fp
fp

## Slide 5: Stack Frame (Arm Arch32 Procedure Call Standards)
Stack Frame Requirements
Minimal frame: at function entry push {fp, lr}
The top two entries in a stack frame are always (1) saved lr, (2) saved fp
sp points at top element in the stack (lowest byte address)
fp points at the lr copy stored in the current stack frame
Stack frames MUST ALWAYS BE aligned to 8-byte addresses
  So, this must always be true: sp % 8 == 0
x
Stack high address
low address
main
main's
frame
saved lr
saved fp
sp
fp
int main(void)
{
a();
/* other code */
return EXIT_SUCCESS;
}
int a(void)
{
int x;
int y;
/* other code */
return 0;
}
a
a's
frame
saved lr
saved fp
sp
fp
high address
low address
saved lr
saved fp
sp
fp
minimal frame above
Always save at least fp and lr
and set fp at saved lr
allocate stack space
SP = SP – "space"
grows "down"
deallocate stack space
SP = SP + "space"
shrinks "up"
preserved registers
Local variables
sp
Note slide has builds
lr & fp must always be at top of frame

## Slide 6: FP_OFF: Distance from FP to SP Used to set FP at push and SP before pop
FP_OFF = (#regs - 1)*4 // -1 is lr offset from sp
Where # regs = #preserved + lr + fp
low memory
4-byte words
sp
saved lr
saved fp
saved r5
saved r4
after push {r4-r7,fp,lr}
add fp, sp, FP_OFF
fp = sp + 20 bytes
saved r7
saved r6
// other code etc .equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF …….
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
# regs saved | FP_OFF in Bytes
2 | 4
3 | 8
4 | 12
5 | 16
6 | 20
7 | 24
8 | 28
9 | 32
Function Prologue
always at top of function saves regs and sets fp
Function Epilogue
always at bottom of function restores regs including the sp
Function Stack Frame
FP_OFF:
Where to set FP after push
Means Caution, odd number of regs!
If odd number pushed, make sure frame is 8-byte aligned (later)
this must always be true: sp % 8 == 0
x
IMPORTANT: FP_OFF has two uses:
Where to set fp after prologue push (remember sp position)
Restore sp (deallocate locals) right before epilogue pop

## Slide 7: Function Prologue and Epilogue: Minimum Stack Frame
x
.global one
.type one, %function
.equ FP_OFF, 4
one:
push {fp, lr}
add fp, sp, FP_OFF // add space for locals
// your code
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr // func return
.size one, (. – one)
Function Prologue always at top of function
Function Epilogue
always at bottom of function
Function Header Assembly directives
Function Footer Assembly directive
Position the fp
low memory
saved lr
saved fp
sp
fp
smallest frame has:
4 bytes between sp & fp
Position the sp
Each function has only one Prologue at the top of the function body and only one Epilogue at the bottom of the function body
When you want to exit the function, set the return value in r0, and then branch (or fall through) to the epilogue
Function entry (Function Prologue):
  save preserved registers
  set the fp to point at saved lr
  allocate space for locals
  (subtracts from sp)
Function return (Function Epilogue):
  deallocate space for locals (adds to sp)
  restores preserved registers
  return to caller

## Slide 8: Function Prologue: Allocating the Stack Frame
saved fp
low memory
saved lr
sp
saved lr
saved fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
saved fp
low memory
saved lr
sp
saved lr
saved fp
callers r5
callers r4
Set FP
add fp, sp, FP_OFF
fp
saved fp
low memory
saved lr
sp
at function entry
saved fp
low memory
saved lr
sp
Local Variables
Allocate Space for locals
ldr r3, =FRMADD
sub sp, sp, r3
saved lr
saved fp
saved r5
saved r4
FRMADD
x
fp
fp
Function was just called this how the stack looks
The orange blocks are part of the caller's stack frame
Function saves lr, fp using a push and only those preserved registers it wants to use on the stack
Do not push r12 or r13
Function moves the fp to point at the saved lr as required by the Aarch32 spec
Allocate Space for Local Variables
fp
Part of function prologue
New Stack Frame
FP_OFF
FP_OFF

## Slide 9: Function Epilogue: Deallocating the Stack Frame
saved fp
low memory
saved lr
sp
Local Variables
At function exit after
pop {r4,r5,fp,lr}
saved lr
saved fp
saved r5
saved r4
Eligible for reuse
out of scope
x
At function exit (in the function epilogue) the function uses pop to restore the registers to the values they had at function entry
fp
Part of function prologue
saved fp
low memory
saved lr
sp
Local Variables
Stack frame while during function body execution
saved lr
saved fp
saved r5
saved r4
FRMADD
fp
FP_OFF
saved fp
low memory
saved lr
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
saved fp
saved r5
saved r4
Deallocated
Move SP back to where it was after the push in the prologue. So, the pop works properly (this also deallocates the local variables)
fp
FP_OFF
Use fp as a pointer to find local variables on the stack

## Slide 10: Review Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
Observation: When a function calls another function, the called function has the right to overwrite the first 4 parameters that were passed to it by the calling function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 11: Accessing argv from Assembly (stderr version)
.extern printf
.extern stderr
.section .rodata
.Lstr: .string "argv[%d] = %s\n"
.text
.global main // main(r0=argc, r1=argv)
.type main, %function
.equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF
ldr r4, =stderr // get the address of stderr
ldr r4, [r4] // get the contents of stderr
ldr r5, =.Lstr // get the address of .Lstr
mov r6, 0 // set indx = 0;
mov r7, r1 // save argv
.Lloop:
// fprintf(stderr, "argv[%d] = %s\n", indx, argv[indx])
ldr r3, [r7] // argv[indx]
cmp r3, 0 // check argv[indx]==NULL
beq .Ldone // if so done
mov r2, r6 // indx
mov r1, r5 // "argv[%d] = %s\n"
mov r0, r4 // stderr
bl fprintf
add r6, r6, 1 // indx++
add r7, r7, 4 // argv++
b .Lloop
.Ldone:
mov r0, 0
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
Function Epilogue
always at bottom of function Branch to this to exit the function restores regs including the sp
argc
**argv
Registers
argv[]
./cipher
in/book
-b
-e
r3
r2
r1
r0
% ./cipher -e -b in/BOOK
argv[0] = ./cipher
argv[1] = -e
argv[2] = -b
argv[3] = in/BOOK
Function Prologue
always at top of function saves regs and sets fp

## Slide 12: Local Variables on the Stack
Local variables are on the stack below the lowest numbered saved register
frame pointer is used as a pointer to stack variables
fp is the base register in ldr and str instructions
Example load buf[0] into r4
  FP_OFF = 12, BUFSZ = 4
  Distance from FP is buf[0] is 12 + 4 = 16
  ldrb r4, [fp, -16]
#define BFSZ 4
int main(void)
{
char buf[BFSZ]; // BFSZ bytes
...
sp
saved lr
saved fp
fp
buf[BFSZ]
BFSZ
FP_OFF
distance from fp to lowest saved register
buf[0]
buf[BFSZ-1]
BFSZ + FP_OFF
x
saved register
saved register
Calculate how much additional space is needed by all the local variables
After the register save push, Subtract from the sp the size of the variable in bytes (+ padding - later slides)

## Slide 13: Function prologue with local variables
move the sp to allocate space on the stack for local variables and outgoing parameters (later)
saved reg
saved reg
sp
fp
Stack after push
saved lr
saved fp
stack frame
x
push {fp, lr}
add fp, sp, FP_OFF
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
FP_OFF
FP_OFF
.equ FRMADD, 8
push {fp, lr}
add fp, sp, FP_OFF
ldr r3, =FRMADD // frames may be large sub sp, sp, r3
// your code
FRMADD
stack frame
size

## Slide 14: Function epilogue with local variables
For pop to restore the registers correctly:
  sp must point at the last saved preserved register put on the stack by the save register operation: the push
x
.equ FRMADD, 8
push {fp, lr}
add fp, sp, FP_OFF ldr r3, =FRMADD sub sp, sp, r3
// your code
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr // func return
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
Return the sp (using the fp) to the same address it had after the push operation sub sp, fp, FP_OFF
this works no matter how much space was allocated in the prologue
FP_OFF
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
FP_OFF
FRMSZ
FRMSZ

## Slide 15: Stack Frame Design – Local Variables
Arrays start at a 4-byte boundary (even arrays with only 1 element)
  Exception: double arrays [ ] start at an 8-byte boundary
  struct arrays are aligned to the requirements of largest member
Space padding (0 or 4 bytes) when necessary is added at the high address end of a variables allocated space, based on the variable's alignment and the requirements of variable below it on the stack
Single chars (and shorts) can be grouped together in same 4-byte word (following the alignment for the short)
After all the variables have been allocated, add padding at stack frame bottom (low memory) so the total stack frame size (including all saved registers) is a multiple of 8 when the prologue is finished
x
A
B
C
D
E
0
pointer
Pad (as needed)
int
a[0]
a[1]
1
2 bytes
integer
short
char
4 bytes

## Slide 16: Step 1: Stack Frame Design – Local Variables
x
int func(void)
{
int x = 0;
short st[2];
char str[] ="ABCDE";
char *ptr = &array[0];
Variable name | Initial Value | Size bytes | Alignment pad to next | Total Size
int x | 0 | 4 | 0 | 4
short a[] | ?? | 2*2 | 0 | 4
char str[] | "ABCDE" | 6 | 2 | 8
char *ptr | &array[0] | 4 | 0 | 4
PAD Added |  | 4 |  | 4
FRMADD (locals etc) | ----- | ----- | ----- | 24
Saved Register Space | ----- | 4 * 4 | --- | 16
Total Frame Size |  |  |  | 40
In this example we are allocating in order of variable definition, no reordering
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
sp
fp
total frame size must divide evenly by 8
4 bytes
saved regs
saved regs
int x
a[0]
a[1]
FRMADD
REG Space

## Slide 17: Accessing Stack Variables The Hard Way…..
Access data stored in the stack
  use ldr/str instructions
Use base register fp with offset (distance in bytes) addressing (either register offset or immediate offset)
No matter where in memory the stack is located, fp always points at saved lr)
Word offset is a way to visualize the distance from fp for calculating offset values
x
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
saved regs
saved regs
int x
a[0]
a[1]
0
1
2
3
4
5
6
7
8
9
Word #
From fp
Variable name | offset from fp | ldr instruction
int x | -16 | ldr r0, [fp, -16]
short a[] | -20 | ldrsh r0, [fp, -20]
char str[] | -28 | ldrb r0, [fp, -28]
char *ptr | -32 | ldr r0, [fp, -32]
fp
[fp, -16]
[fp, -20]
[fp, -28]
[fp, -32]
[fp, -12]
FP_OFF = 12
sp or[fp,-36]
4
4
4
4
8

## Slide 18: Step 2 Generate Distance offsets from [fp]
x
sp
fp
[fp, -FP_OFF]
[fp, -X]
[fp, -A]
[fp, -STR]
[fp, -PTR]
[fp, -PAD]
12 bytes
4
4
8
4
4
FRMADD = PAD – FP_OFF
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
saved regs
saved regs
int x
a[0]
a[1]
Variable name | Size | Name | expression size + prev | Distance from fp
Pushed regs-1 | 12 | FP_OFF |  | 12
int x | 4 | X | 4 + FP_OFF | 16
short a[] | 4 | A | 4 + X | 20
char str[] | 8 | STR | 8 + A | 28
char *ptr | 4 | PTR | 4 + STR | 32
PAD Added | 4 | PAD | 4 + PTR | 36
FRMADD |  | FRMADD | PAD-FP_OFF | 24
Use the assembler to calculate the distance from the address contained in fp [fp, -offset]
.equ FP_OFF, 12
.equ X, 4+FP_OFF // X = 16
.equ A, 4+X // A = 20
Assign label names for each local variable
  Each name is .equ to be the offset from fp

## Slide 19: Step 3 Allocate Space in the Prologue
x
.global func
.type func, %function
.equ FP_OFF, 12
.equ X, 4 + FP_OFF
.equ A, 4 + X
.equ STR, 8 + A
.equ PTR, 4 + STR
.equ PAD, 4 + PTR
.equ FRMADD PAD - FP_OFF
func:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
ldr r3, =FRMADD //frames can be large
sub sp, sp, r3 // add space for locals
// rest of function code
// no change to epilogue
sub sp, fp, FP_OFF // deallocate locals
pop {r4, r5, fp, lr}
bx lr
.size func, (. – func)
sp
fp
[fp, -FP_OFF]
[fp, -X]
[fp, -A]
[fp, -STR]
[fp, -PTR]
[fp, -PAD]
12 bytes
4
4
8
4
4
FRMADD = PAD – FP_OFF
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
saved regs
saved regs
int x
a[0]
a[1]

## Slide 20: Accessing Stack using distance offsets
x
var | how to get the address | how to read contents
x | ldr r0, =X sub r0, fp, r0 | ldr r0, =X ldr r0, [fp, -r0]
a[0] | ldr r0, =A sub r0, fp, r0 | ldr r0, =A ldrsh r0, [fp, -r0]
a[1] | ldr r0, =A - 2 sub r0, fp, r0 | ldr r0, =A - 2 ldrsh r0, [fp, -r0]
str[1] | ldr r0, =STR - 1 sub r0, fp, r0 | ldr r0, =STR - 1 ldrb r0, [fp, -r0]
ptr | ldr r0, =PTR sub r0, fp, r0 | ldr r0, =PTR ldr r0, [fp, -r0]
*ptr | ldr r0, =PTR sub r0, fp, r0 ldr r0, [r0] | ldr r0, =PTR ldr r0, [fp, -r0] ldr r0, [r0]
sp
fp
[fp, -FP_OFF]
[fp, -X]
[fp, -A]
[fp, -STR]
[fp, -PTR]
[fp, -PAD]
12 bytes
4
4
8
4
4
FRMADD = PAD – FP_OFF
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
saved regs
saved regs
int x
a[0]
a[1]
var | how to write contents
ptr | ldr r0, =PTR str r1, [fp, -r0]
*ptr | ldr r0, =PTR ldr r0, [fp, -r0] str r1, [r0]

## Slide 21: Step 4 Initialize the Local Variables
x
mov r4, 0
ldr r5, =X
str r4, [fp, -r5]
ldr r5, =STR
sub r5, fp, r5 // r5 = addr of STR
ldr r4, =PTR
str r5, [fp, -r4] //ptr = &(str[0])
mov r4, 'A'
strb r4, [r5]
mov r4, 'B'
add r5, r5, 1
strb r4, [r5]
//…
sp
fp
[fp, -FP_OFF]
[fp, -X]
[fp, -A]
[fp, -STR]
[fp, -PTR]
[fp, -PAD]
12 bytes
4
4
8
4
4
FRMADD = PAD – FP_OFF
A
B
C
D
E
0
pointer ptr
Pad 4 bytes
saved lr
saved fp
saved regs
saved regs
int x
a[0]
a[1]
int func(void)
{
int x = 0;
short st[2];
char str[] ="ABCDE";
char *ptr = &(str[0]);

## Slide 22: C Stream Functions Array/block read/write
Read/write ops advance the file position pointer from TOF towards EOF on each I/O
  Moves towards EOF by number of bytes read/written
  size_t fwrite(void *ptr, size_t size, size_t count, FILE *stream);
  Writes an array *ptr of count elements of size bytes from stream
  Updates the write file pointer forward by the number of bytes written
  returns number of elements written
    Treat return != count as an error
  size_t fread(void *ptr, size_t size, size_t count, FILE *stream);
  Reads an array *ptr of count elements of size bytes from stream
  Updates the read file pointer forward by the number of bytes read
  returns number of elements read,
    Treat a return of 0 as being in EOF state
Set element size to 1 to return bytes read/written
EOF is NOT a character in the file, but a condition on the stream
int feof(FILE *stream)
  Returns non-zero at end-of-file for stream
int ferror(FILE *stream)
  Returns non-zero if error for stream
x
file
Old file position pointer
New file position pointer
read or write N
bytes/chars

## Slide 23
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.10
Lecture 21 – December 1, 2022
Aarch32 Assembly – Part 5
Frontier Exascale

## Slide 24: Passing Pointers to Stack Variables
#include <stdio.h>
#include <stdlib.h>
#include <errno.h>
#define BUFSZ 4096 // copies input to output
int
main(void) {
char buf[BUFSZ];
size_t cnt; // assign to a register only
// read from stdin, up to BUFSZ bytes
// and store them in buf
// Number of bytes read is in cnt
while ((cnt = fread(buf, 1, BUFSZ, stdin)) > 0) {
// write cnt bytes from buf to stdout
if (fwrite(buf, 1, cnt, stdout) != cnt) {
return EXIT_FAILURE;
}
}
return EXIT_SUCCESS;
}
sp
saved lr
saved fp
fp
buf[BUFSZ]
buf[0]
saved r4
saved r5
saved r6
saved r7
.text
.global main
.type main, %function // stack frame below
.equ BUFSZ, 4096
.equ FP_OFF, 20 // fp offset in main stack frame
.equ BUF, BUFSZ+FP_OFF// buffer
.equ PAD, 0+BUF // Stack frame PAD
.equ FRMADD, PAD-FP_OFF // space for locals+passed args
FILE *
Data Segment
Global Variables
FILE *
stdin:
stdout:
struct
struct

## Slide 25: Reading and Writing bytes using C library routines fread() and fwrite()
// fread(buffer, element_size, number of elements, FILE *)
// fread(r0=buf, r1=1, r2=BUFSZ, r3=stdin)
mov r0, r4 // buf
mov r1, 1 // bytes
mov r2, BUFSZ // cnt (or ldr r2, =BUFSZ)
mov r3, r5 // stdin
bl fread
cmp r0, 0 // check return value from fread
// fwrite(buffer, element_size, number of elements, FILE *)
// fwrite(r0=buf, r1=1, r2=cnt, r3=stdout)
mov r0, r4 // buf
mov r1, 1 // bytes
mov r2, r7 // cnt
mov r3, r6 // stdout
bl fwrite
cmp r0, r7 // check return value from fwrite
// save values in preserved registers
ldr r4, =BUF // distance from fp
sub r4, fp, r4 // pointer to buffer
ldr r5, =stdin // standard input global
ldr r5, [r5]
ldr r6, =stdout // standard output global
ldr r6, [r6]
sp
saved lr
saved fp
fp
buf[BUFSZ]
buf[0]
saved r4
saved r5
saved r6
saved r7
BUF=
FP_OFF +
BUFSZ
.text
.global main
.type main, %function // stack frame below, distances from fp
.equ BUFSZ, 4096
.equ FP_OFF, 20 // fp offset in main stack frame
.equ BUF, BUFSZ+FP_OFF// buffer
.equ PAD, 0+BUF // Stack frame PAD
.equ FRMADD, PAD-FP_OFF // space for locals+passed args
FP_OFF
BUFSZ

## Slide 26: Passing Pointers to Stack Variables
#define BUFSZ 4096
int main(void) {
char buf[BUFSZ];
size_t cnt; // assign to a register only
while ((cnt = fread(buf, 1, BUFSZ, stdin)) > 0) {
if (fwrite(buf, 1, cnt, stdout) != cnt) {
return EXIT_FAILURE;
}
}
return EXIT_SUCCESS;
}
.extern fread
.extern fwrite
.extern stdin
.extern stdout
.equ EXIT_FAILURE, 1
.text
.global main
.type main, %function
.equ BUFSZ, 4096
.equ FP_OFF, 20
.equ BUF, BUFSZ + FP_OFF
.equ PAD, 0 + BUF
.equ FRMADD, PAD-FP_OFF
// see right --
.Ldone:
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
.size main, (. - main)
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF // set frame pointer
ldr r3, =FRMADD // get frame size
sub sp, sp, r3 // allocate space
// save values in preserved registers
ldr r4, =BUF // distance from fp
sub r4, fp, r4 // pointer to buffer
ldr r5, =stdin // standard input global
ldr r5, [r5]
ldr r6, =stdout // standard output global
ldr r6, [r6]
.Lloop:
// fread(r0=buf, r1=1, r2=BUFSZ, r3=stdin)
mov r0, r4 // buf
mov r1, 1 // bytes
mov r2, BUFSZ // cnt (or ldr r2, =BUFSZ)
mov r3, r5 // stdin
bl fread
cmp r0, 0
ble .Ldone
mov r7, r0 // save cnt
// fwrite(r0=buf, r1=1, r2=cnt, r3=stdout)
mov r0, r4 // buf
mov r1, 1 // bytes
mov r2, r7 // cnt
mov r3, r6 // stdout
bl fwrite
cmp r0, r7 // did we write all the bytes?
beq .Lloop
mov r0, EXIT_FAILURE
.Ldone:

## Slide 27: Writing Functions: Receiving a Pointer Parameter - 1
#define BFSZ 256
void fillbuf(char *s, int len, char fill);
int main(void)
{
char buf[BFSZ];
fillbuf(buf, BFSZ, 'A');
return EXIT_SUCCESS;
}
sp
saved lr
saved fp
fp
buf[BFSZ]
BFSZ
FP_OFF
buf[0]
buf[BFSZ-1]
BFSZ + FP_OFF
r0, r1, r2
x
void fillbuf(char *s, int len, char fill)
{
char *enptr = s + len;
while (*s < enptr)
*(s++) = fill;
}
sp
saved lr
saved fp
fp
buf[BFSZ]
buf[0]
buf[BFSZ-1]
saved lr
saved fp
r0 points at caller's frame
r1
r0, r1, r2

## Slide 28: Writing Function: Receiving a Pointer Parameter - 2
x
sp
saved lr
saved fp
fp
buf[BFSZ]
buf[0]
buf[BFSZ-1]
saved lr
saved fp
r0
r1
void
fillbuf(char *s, int len, char fill)
{
char *enptr = s + len;
while (s < enptr)
*(s++) = fill;
}
r0, r1, r2
fillbuf:
push {fp, lr} // stack frame
add fp, sp, FP_OFF // set fp to base
add r1, r1, r0 // copy up to r1 = bufpt + cnt
cmp r0, r1 // are there any chars to fill?
bge .Ldone // nope we are done
.Ldowhile:
strb r2, [r0] // store the char in the buffer
add r0, 1 // point to next char
cmp r0, r1 // have we reached the end?
blt .Ldowhile // if not continue to fill
.Ldone:
sub sp, fp, FP_OFF // restore stack frame top
pop {fp, lr} // restore registers
bx lr // return to caller
Using r1 for endptr

## Slide 29: Passing More Than Four Arguments – At the point of Call
Args > 4 are in the caller's stack frame at SP (argv5), an up
Called functions have the right to change stack args just like they can change the register args!
  Caller must assume all args including ones on the stack are changed by the caller
Calling function prior to making the call
  Evaluate first four args: place resulting values in r0-r3
  Store Arg 5 and greater parameter values on the stack
One arg value per slot! – NO arrays across multiple slots
  chars, shorts and ints are directly stored
  Structs (not always), and arrays are passed via a pointer
  Pointers passed as output parameters usually contain an address that points at the stack, BSS, data, or heap
arg 5
sp
saved lr
saved fp
arg 6
arg n
arg 1 & return
arg 2
arg 3
arg 4
r0
r1
r2
r3
r0 = function(r0, r1, r2, r3, arg5, arg6, … argn)
arg1, arg2, arg3, arg4, ...
Temporary Registers
fp
….
calling functions stack frame
Stack segment
high memory
x
saved regs
local
variables
PAD (if needed)

## Slide 30: Calling Function: Allocating Stack Parameter Space
At the point of a function call (and obviously at the start of the called function):
sp must point at arg5
arg5 must be at an 8-byte boundary,
  padding to force arg5 alignment is placed above the last argument the called function is expecting
Approach: Extend the stack frame to include enough space for stack arguments function with the greatest arg count
Examine every function call in the body of a function
Find the function call with greatest arg count, Determines space needed for outgoing args
Add the space needed to the frame layout
arg 5
sp
arg 6
arg 7
arg 8
arg 9
Outgoing arg space part of calling functions frame
saved lr
saved fp
rest of frame
fp
Preserved registers
local vars
Rules: At point of call
arg5 must be pointed at by sp
SP must be 8-byte aligned
x
Callers stack frame
Previous stack frame
PAD (if needed)

## Slide 31: Calling Function: Pass ARGS 5 and higher
oarg5
sp
oarg6
oarg7
oarg8
oarg9
PAD
Outgoing arg space part of calling functions frame
saved lr
saved fp
cnt[2]
fp
Preserved registers
local vars
Rules: At point of call
arg5 must be pointed at by sp
SP must be 8-byte aligned
x
Callers stack frame
Previous stack frame
var | write contents
OARG5 = r1 | ldr r0, =OARG5 //distance str r1, [fp, -r0]
OARG6 = &cnt | ldr r2, =CNT //distance sub r2, fp, r2 // &cnt ldr r0, =OARG6 //distance str r2, [fp, -r0]
.equ FP_OFF, 4
.equ CNT, 8 + FP_OFF // int cnt[2];
.equ PAD, 4 + CNT // added as needed
.equ OARG9, 4 + PAD
.equ OARG8, 4 + OARG9
.equ OARG7, 4 + OARG8
.equ OARG6, 4 + OARG7
.equ OARG5, 4 + OARG6
.equ FRMADD OARG5 – FP_OFF

## Slide 32: Called Function: Retrieving Args From the Stack
At function start and before the push{} the sp is at an 8-byte boundary
Args are in the caller's stack frame and arg 5 always starts at fp+4
  Additional args are higher up the stack, with one “slot” every 4-bytes
This "algorithm" for finding args was designed to enable variable arg count functions like printf("conversion list", arg0, … argn);
Rule: Called functions always access stack parameters using a positive offset to the fp
Constant | Offset | arm ldr /str statement
ARGN | (N-4)*4 | ldr r4, [fp, ARGN]
ARG9 | 20 | ldr r4, [fp, ARG9]
ARG8 | 16 | ldr r4, [fp, ARG8]
ARG7 | 12 | ldrb r4, [fp, ARG7]
ARG6 | 8 | ldr r4, [fp, ARG6]
ARG5 | 4 | ldrh r4, [fp, ARG5]
int func(int a1, int a2, int a3, int a4,
short a5, int a6, char a7, int a8, int a9)
x
.equ ARG9, 20
.equ ARG8, 16
.equ ARG7, 12
.equ ARG6, 8
.equ ARG5, 4
Callers Stack frame
no defined limit to number of args, keep going up stack 4 bytes at a time
lr to caller
callers fp
fp
sp
fp+12
fp+16
fp+20
fp+8
fp+4
arg5
arg6
arg7
arg8
arg9
PAD
???
???
Local variables
Current Stack Frame
Saved Registers
saved lr
saved fp
rest of frame

## Slide 33: Determining the Passed Parameter Area on The Stack
Find the function called by main with the largest number of parameters
That function determines the size of the Passed Parameter allocation on the stack
int main(void)
{
/* code not shown */
a(g, h);
/* code not shown */
sixsum(a1, a2, a3, a4, a5, a6);
/* code not shown */
b(q, w, e, r);
/* code not shown */
}
largest arg count is 6
allocate space for 6 - 4 = 2 arg slots
x

## Slide 34: Passing More than Four Args – Six Arg Example
Problem: Write and call a function that receives six integers and returns the sum
First 4 parameters are in register r0 - r3 and the remaining argument are on the stack
For this example, we will put all the locals on the stack
int main(void)
{
int cnt = sixsum(1, 2, 3, 4, 5, 6);
printf("the sum is %d\n", cnt);
return EXIT_SUCCESS;
}
int
sixsum(int a1, int a2, int a3, int a4, int a5, int a6)
{
return a1 + a2 + a3 + a4 + a5 + a6;
}
x

## Slide 35: Calling Function > 4 Args - 1
pad
saved lr
saved fp
fp
sp
x
.equ FP_OFF, 12 // local base
// NAME, SIZE + prev_name
.equ CNT, 4 + FP_OFF
.equ PAD, 4 + CNT
.equ OARG6, 4 + PAD
.equ OARG5, 4 + OARG6
.equ FRMADD OARG5 – FP_OFF
int cnt = sixsum(1, 2, 3, 4, 5, 6);
cnt
oarg5
oarg6
Callers stack frame
saved r4
saved r5

## Slide 36: Calling Function > 4 Args - 2
x
.equ FP_OFF, 12
.equ CNT, 4 + FP_OFF
.equ PAD, 4 + CNT
.equ OARG6, 4 + PAD
.equ OARG5, 4 + OARG6
.equ FRMADD OARG5 – FP_OFF
main:
push {r4, r5, fp, lr}
add fp, sp, FP_OFF
ldr r3, =FRMADD
sub sp, sp, r3
mov r0, 6
ldr r5, =OARG6
str r0, [fp, -r5] // arg6
mov r0, 5
ldr r5, =OARG5
str r0, [fp, -r5] // arg5
mov r3, 4 // arg4
mov r2, 3 // arg3
mov r1, 2 // arg2
mov r0, 1 // arg1
bl sixsum
ldr r5, =CNT
str r0, [fp, -r5] // update cnt on stack
mov r1, r0
ldr r0, =.Lpfstr
bl printf
mov r0, EXIT_SUCCESS
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
int cnt = sixsum(1, 2, 3, 4, 5, 6);
fp - OARG5
fp - OARG6
fp - PAD
fp - CNT
pad
saved lr
saved fp
fp
sp
cnt
oarg5
oarg6
Callers stack frame
saved r4
saved r5
.section .rodata
.Lpfstr: .string "the sum is %d\n"

## Slide 37: Called Function > 4 Args
pad
saved lr
saved fp
fp
sp
x
.equ ARG6, 8 // offset into caller's frame
.equ ARG5, 4 // offset into caller's frame
.equ FP_OFF, 4 // local base
cnt
oarg5
sixsum:
push {fp, lr}
add fp, sp, FP_OFF
add r0, r0, r1
add r0, r0, r2
  add r0, r0, r3
ldr r1, [fp, ARG5]
add r0, r0, r1
ldr r1, [fp, ARG6]
add r0, r0, r1
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
oarg6
int sixsum(int a1, int a2, int a3, int a4, int a5, int a6)
return a1 + a2 + a3 + a4 + a5 + a6;
saved lr
saved fp
fp + ARG5
fp + ARG6
Callers stack frame
Current stack frame
saved r4
saved r5

## Slide 38: Extra Slides

## Slide 39: Local Variables: Stack Frame Design Practice
short a[3];
short *ptr1;
char tmp;
char *ptr2;
char nm[] = "cse30";
pad
ptr1
tmp
pad
ptr2
pad
a[2]
a[1]
a[0]
saved lr
saved fp
fp
sp
x
'c'
's'
'e'
'3'
'0'
'\0'
pad
When writing real code, you do not have to put all locals on the stack
Place locals in registers if they fit, are accessed often, and
You do not need their address (they are not an output variable in a function call)
.equ FP_OFF, 4 // Local base
// NAME, SIZE + prev_name
.equ A, 8 + FP_OFF
.equ PTR1, 4 + A
.equ TMP, 4 + PTR1
.equ PTR2, 4 + TMP
.equ NM, 8 + PTR2
.equ PAD, 4 + NM
.equ FRMADD PAD – FP_OFF // for locals
1
2
3
4
5
6
7
8
9
10
[fp, -FP_OFF]
Example shows allocation without reordering variables to optimize space
FRMADD

## Slide 40: Local Variables: Stack Frame Design Reordering
short a[3];
short *ptr1;
char *ptr2;
char tmp;
char nm[] = "cse30";
ptr1
tmp
ptr2
pad
a[2]
a[1]
a[0]
saved lr
saved fp
fp
sp
x
'c'
's'
'e'
'3'
'0'
'\0'
pad
When writing real code, you do not have to put all locals on the stack
Place locals in registers if they fit, are accessed often, and
You do not need their address (they are not an output variable in a function call)
.equ FP_OFF, 4 // Local base
// NAME, SIZE + prev_name
.equ A, 8 + FP_OFF
.equ PTR1, 4 + A
.equ PTR2, 4 + PTR1
.equ TMP, 2 + PTR2
.equ NM, 6 + TMP
.equ PAD, 0 + NM // not needed
.equ FRMADD PAD – FP_OFF
1
2
3
4
5
6
7
8
[fp, -FP_OFF]
Example shows allocation with reordering variables to optimize space
Alternative
location
size change

## Slide 41: ARM Assembly Source File: Header and Footer
.syntax unified
  use the standard ARM assembly language syntax called Unified Assembler Language (UAL)
.section .note.GNU-stack,"",%progbits
  tells the linker to make the stack and all data segments not-executable (no instructions in those sections) – security measure
.end
  at the end of the source file, everything written after the .end is ignored
.arch armv6 // armv6 architecture
.arm // arm 32-bit instruction set
.fpu vfp // floating point co-processor
.syntax unified // modern syntax
File Header
At the top of every ARM source file
.section .note.GNU-stack,"",%progbits // set stack/data non-exec
.end
// everything past the .end is ignored!
// Debugging notes etc
File Footer
At the bottom of every ARM source file
// Contents of the other memory segment include .text (your code)
x

## Slide 42: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  In CSE30 required use: .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x

## Slide 43: Reference For PA8/9: C Stream Functions Opening Files
FILE *fopen(char filename[], const char mode[]);
Opens a stream to the specified file in specified file access mode
  returns NULL on failure – always check the return value; make sure the open succeeded!
Mode is a string that describes the actions that can be performed on the stream:
''r’" Open for reading.
The stream is positioned at the beginning of the file. Fail if the file does not exist.
''w" Open for writing.
The stream is positioned at the beginning of the file. Create the file if it does not exist.
''a" Open for writing.
The stream is positioned at the end of the file. Create the file if it does not exist.
Subsequent writes to the file will always be at current end of file.
An optional ''+'' following ''r'', ''w'', or ''a'' opens the file for both reading and writing
x

## Slide 44: Reference: C Stream Functions Closing Files and Usage
int fclose(FILE *stream);
  Closes the specified stream, if open for writing, then forcing output to complete (eventually)
    returns EOF on failure (often ignored as no easy recovery other than a message)
Usage template for fopen() and fclose()
  Open a file with fopen() always checking the return value
  do i/o – keep calling stdio io routines
  close the file with fclose() when done with that I/O stream
x

## Slide 45: C Stream Functions Array/block read/write
Read/write ops advance the file position pointer from TOF towards EOF on each I/O
  Moves towards EOF by number of bytes read/written
  size_t fwrite(void *ptr, size_t size, size_t count, FILE *stream);
  Writes an array *ptr of count elements of size bytes from stream
  Updates the write file pointer forward by the number of bytes written
  returns number of elements written
    Treat return != count as an error
  size_t fread(void *ptr, size_t size, size_t count, FILE *stream);
  Reads an array *ptr of count elements of size bytes from stream
  Updates the read file pointer forward by the number of bytes read
  returns number of elements read,
    Treat a return of 0 as being in EOF state
Set element size to 1 to return bytes read/written
EOF is NOT a character in the file, but a condition on the stream
int feof(FILE *stream)
  Returns non-zero at end-of-file for stream
int ferror(FILE *stream)
  Returns non-zero if error for stream
x
file
Old file position pointer
New file position pointer
read or write N
bytes/chars

## Slide 46: putchar/getchar Setting up and Usage
.extern getchar
.extern putchar
.section .rodata
.Lfstr: .string "Echo count: %d\n"
.text
.equ EOF, -1
.type main, %function
.global main .equ FP_OFF, 12
.equ EXIT_SUCCESS, 0
main: push {r4, r5, fp, lr}
add fp, sp, FP_OFF
mov r4, 0 //r4 = count
/* while loop code will go here */
.Ldone:
mov r1, r4 // count
ldr r0, =.Lfstr
bl printf
mov r0, EXIT_SUCCESS
sub sp, fp, FP_OFF
pop {r4, r5, fp, lr}
bx lr
.size main, (. – main)
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int c;
int count = 0;
while ((c = getchar()) != EOF) {
putchar(c);
count++;
}
printf("Echo count: %d\n”, count);
return EXIT_SUCCESS;
}
r0 r1
x

## Slide 47: Putchar/getchar: The while loop
mov r4, 0 //count
bl getchar
cmp r0, EOF
beq .Ldone
.Lloop:
bl putchar
bl getchar
add r4, r4, 1
cmp r0, EOF
bne .Lloop
.Ldone:
mov r1, r4
ldr r0, =pfstr
bl printf
#include <stdio.h>
#include <stdlib.h>
int
main(void)
{
int c;
int count = 0;
while ((c = getchar()) != EOF) {
putchar(c);
count++;
}
printf("Echo count: %d\n”, count);
return EXIT_SUCCESS;
}
pre loop test with a call to getchar()
if it returns EOF in r0 we are done
File header and footers are not shown
echo the character read with getchar and then read another and increment count
initialize count
did getchar() return EOF if not loop
saw EOF, print count
x

## Slide 48: printing error messages in assembly
x
// int errmsg(char *errormsg)
// writes error messages to stderr
.type errmsg, %function // define to be a function
.equ FP_OFF, 4 // fp offset in stack frame
errmsg:
push {fp, lr} // stack frame register save
add fp, sp, FP_OFF // set the frame pointer
mov r1, r0
ldr r0, =stderr
ldr r0, [r0]
bl fprintf
mov r0, EXIT_FAILURE // Set return value
sub sp, fp, FP_OFF // restore stack frame top
pop {fp, lr} // remove frame and restore
bx lr // return to caller
// function footer
.size errmsg, (. - errmsg) // set size for function
.Lmsg0: .string "Read failed\n"
ldr r0, =.Lmsg0 // read failed print error
bl errmsg

## Slide 49: main.S Source File Showing a minimum stack frame
.arch armv6
.arm
.fpu vfp
.syntax unified
// BSS Segment (only when needed)
.bss
// Data Segment (only when needed)
.data
// Read-Only Data (only when needed)
.section .rodata
// Text Segment – your code
.text
.type main, %function
.global main
.equ FP_OFF, 4
.equ EXIT_SUCCESS, 0
main:
push {fp, lr}
add fp, sp, FP_OFF
// main() code goes here
mov r0, EXIT_SUCCESS
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr
.size main, (. – main)
.section .note.GNU-stack,"",%progbits
.end
function header
+ prologue constant
function epilogue
function footer
function return value in r0
“branch” (return) to caller
function prologue
file footer
x
file header
4 is for minimum stack frame this will vary