## Slide 1
UCSD CSE 30
Keith Muller
Computer Organization and Systems Programming
Version 1.04
Lecture 19 – November 22, 2022
Aarch32 Assembly – Part 4

## Slide 2: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
1
0xfff0
Stack

## Slide 3: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
factorial
n:
1
0xfff0
Stack
4
factorial
n:
3
factorial
n:
2
factorial
n:
1
Returns 1

## Slide 4: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
factorial
n:
1
0xfff0
Stack
4
factorial
n:
3
factorial
n:
2
Returns 2
factorial
n: 1
Out of scope

## Slide 5: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
factorial
n:
1
0xfff0
Stack
4
factorial
n:
3
Returns 6
factorial
n: 2
factorial
n: 1
Out of scope

## Slide 6: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
factorial
n:
1
0xfff0
Stack
4
Returns 24
factorial
n: 3
factorial
n: 2
factorial
n: 1
Out of scope

## Slide 7: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
1
0xfff0
Stack
factorial
n: 4
factorial
n: 3
factorial
n: 2
factorial
n: 1
Out of scope

## Slide 8: The Stack
Memory
0x0
main
argc:
argv:
Each function call has its own stack frame for its own copy of variables.
  int factorial(int n) {
  if (n == 1) {
  return 1;
  } else {
  return n * factorial(n – 1);
  }
  }
  int main(int argc, char *argv[]) {
  printf("%d", factorial(4));
  return 0;
  }
1
0xfff0
Stack
factorial
n: 4
factorial
n: 3
factorial
n: 2
factorial
n: 1
Out of scope
printf
"%d"
return factorial(4)

## Slide 9: Ghost of Stack Frames Past…..
void ghost(int n)
{
int x;
int y;
printf("before ghost: %d %d\n", x, y);
x = 10*n;
y = 100*n;
printf("after ghost: %d %d\n", x, y);
return;
}
void wraith (void)
{
int a;
int b;
printf("wraith: %d %d\n", a, b);
return;
}
int main(void)
{
ghost(3);
wraith();
return EXIT_SUCCESS;
}
% ./a.out
before ghost: 0 66328
after ghost: 30 300
wraith: 30 300
%
See how wraith has the old values left over from the prior call to ghost
same stack frame variable layout
x

## Slide 10: Function Header and Footer Assembler Directives
.global function_name
  Exports the function name to other files. Required for main function, optional for others
.type name, %function
  The .type directive sets the type of a symbol/label name
  %function specifies that name is a function (name is the address of the first instruction)
equ FP_OFF, 4
  Used for basic stack frame setup; the number 4 will change – later slides
.size name, bytes
  The .size directive is used to set the size associated with a symbol
  Used by the linker to exclude unneeded code and/or data when creating an executable file
  It is also used by the debugger gdb
  bytes is best calculated as an expression: (period is the current address in a memory segment)
  In CSE30 required use: .size name, (. – name)
.text
.global myfunc // make myfunc global for linking
.type myfunc, %function // define myfunc to be a function
.equ FP_OFF, 4 // fp offset in main stack frame
myfunc:
// function prologue, stack frame setup
    // your code
// function epilogue, stack frame teardown
.size myfunc, (. – myfunc)
function entry point
address of the first instruction in the function
Must not be a local label (does not start with .L)
Function Header
Function Footer
x

## Slide 11: Support For Function Calls and Function Call Return - 1
Branch with Link (function call) instruction
bl label
Function call to the instruction with the address label (no local labels for functions)
  imm24 number of instructions from pc+8
label any function label in the current ﬁle, or any function label that is deﬁned as .global in any ﬁle that it is linked to
BL saves the address of the instruction immediately following the bl instruction in register lr (link register is also known as r14)
The contents of the link register is the return address in the calling function
bl
imm24
x
main:
●
bl f1 f1:
● ●
(1) Branch to the instruction with the label f1
(2) copies the address of the instruction AFTER the bl in lr

## Slide 12: Support For Function Calls and Function Call Return - 2
Branch & exchange (function return) instruction
bx lr // we will always use lr
Causes a branch to the instruction whose address is stored in register <lr>
  It copies lr to the PC
This is often used to implement a return from a function call (exactly like a C return) when the function is called using bl label
bx
Rn
main:
●
●
bl f1 f1: ●
● ●
● bx lr
●
Branch to the instruction whose address is stored in lr
x
Stores this address in lr
this is the address to resume at in the caller

## Slide 13: bl and bx operation working together
int main(void)
{
a();
// other code
a();
return EXIT_SUCCESS;
}
int a(void)
{
// other code
return 0;
}
.text
.type main, %function
.global main
.equ EXIT_SUCCESS, 0
main:
// code
bl a
// other code
bl a
mov r0, EXIT_SUCCESS
// code
bx lr
.size main, (. - main)
.type a, %function
a:
// code
mov r0, 0
// code
bx lr
.size a, (. - a)
ra1
ra2
lr
ra1
lr
ra2
lr
ra1
lr
ra2
●
●
●
bl a a: ●
● ●
● bx lr
bl a
●
●
address of
next instruction
is stored in lr
address of
next instruction
is stored in lr
x
But there is a problem we must address here – see next slide

## Slide 14: Preserving lr (and fp): The Foundation of a stack frame
int main(void)
{
a();
/* other code */
return EXIT_SUCCESS;
}
int a(void)
{
b();
/* other code */
return 0;
}
int b(void)
{
/* other code */
return 0;
}
● ● ● bl a ● ● ● | a: ● ● ● bl b ● ● ● bx lr | b: ● ● bx lr
Saves the return address in LR
x
Saves the return address in LR
Copies the saved return address from lr back into pc
Copies the saved return address from lr back into pc
Uh No
Infinite loop!!!
Modifies the link register (lr), writing over main's return address – with the instruction following! Cannot return to main()

## Slide 15: Preserving lr (and fp): The Foundation of a stack frame
● ● ● bl a ● ● ● | a: ● ● ● bl b ● ● ● bx lr | b: ● ● bx lr
Fix: Save the contents of fp, lr on the stack.
Restores the contents of fp, lr from the stack.
push {fp, lr}
pop {fp, lr}
Saves the return address in LR
Copies the saved return address from lr back into pc
push {fp, lr}
pop {fp, lr}
x
The frame pointer is used to find variables on the stack – later
int main(void)
{
a();
/* other code */
return EXIT_SUCCESS;
}
int a(void)
{
b();
/* other code */
return 0;
}
int b(void)
{
/* other code */
return 0;
}
Restores the contents of fp, lr from the stack.
Fix: Save the contents of fp, lr on the stack.
Copies the saved return address from lr back into pc

## Slide 16: Review Return Value and Passing Parameters to Functions (Four parameters or less)
Where r0, r1, r2, r3 are arm registers, the function declaration is (first four arguments):
r0 = function(r0, r1, r2, r3) // 32-bit return
r0, r1 = function(r0, r1, r2, r3) // 64-bit return – long long
Each parameter and return value is limited to data that can fit in 4 bytes or less
You receive up to the first four parameters in these four registers
You copy up to the first four parameters into these four registers before calling a function
For parameter values using more than 4 bytes, a pointer to the parameter is passed (we will cover this later)
You MUST ALWAYS assume that the called function will alter the contents of all four registers: r0-r3
Observation: When a function calls another function, the called function has the right to overwrite the first 4 parameters that were passed to it by the calling function
Register | Function Call Use
r0 | 1st parameter
r1 | 2nd parameter
r2 | 3rd parameter
r3 | 4th parameter
Register | Function Return Value Use
r0 | 8, 16 or 32-bit result, 32-bit address or least-significant half of a 64-bit result
r1 | most-significant half of a 64-bit result
x

## Slide 17: Argument and Return Value Requirements
When passing or returning values from a function you must do the following:
Make sure that the values in the registers r0-r3 are in their properly aligned position in the register based on data type
Upper bytes in byte and halfword values in registers r0-r3 when passing arguments and returning values are zero filled
0x00
0x00
0x00
0xe1
0
31
Single Byte
r0
0x00
0x00
0xe3
0xe1
0
31
r0
Single Halfword
0x87
0x65
0xe3
0xe1
0
31
r0
Full Word
observe the zero fill
observe the zero fill

## Slide 18: Preserved Registers: Protocols for Use
Function Call Spec:
Preserved registers will not be changed by any function you call
Interpretation: Any value you have in a preserved register before a function call will still be there after the function returns
Contents are “preserved” across function calls
If the function wants to use a preserved register it must:
Save the value contained in the register at function entry
Use the register in the body of the function
Restore the original saved value to the register at function exit (before returning to the caller)
Register | Function Call Use | Function Body Use | Save before use Restore before return
r4-r10 |  | contents preserved across function calls | Yes
r7 | os system call number | contents preserved across function calls | Yes
r12, r15 | Done not use |  | 
x

## Slide 19: Preserved Registers: When to Use?
When to use a preserved register in a function you are writing:
Values that you want to protect from being changed by a function call
  Local variables stored in registers
  Parameters passed to you (in r0-r3) that you need to continue to use after calling another function
Need more than r0-r3 whether you call another function or not
Options are:
  preserved register or
  stack local variable (later slides)
Register | Function Call Use | Function Body Use | Save before use Restore before return
r4-r10 |  | contents preserved across function calls | Yes
r7 | os system call number | contents preserved across function calls | Yes
r12, r15 | Done not use |  | 
x

## Slide 20: Preserving and Restoring Registers by copying to/from Stack Moves sp to allocate (Push) or deallocate (pop) stack space
high memory
low memory
before
stack pointer
push{ }
after
stack pointer
pop{ }
after stack pointer
before stack
pointer
high memory
low memory
Operation | Pseudo Instruction (Use in CSE30) |  | ARM instruction (reference only) | Operations
Push registers onto stack Function Entry | push | {reg list} | stmfd sp!, {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers from stack Function Exit | pop | {reg list} | ldmfd sp!, {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers
x
registers
registers
registers
registers
registers
registers
push (multiple register str to memory operation)
push (multiple register ldr from memory operation)

## Slide 21: Preserving and Restoring Registers on the Stack Function entry and Function exit
Where {reg list} is a list of registers in numerically increasing order
example: push {r4-r10, fp, lr}
Registers cannot be: (1) duplicated in the list, nor be (2) listed out of numeric order
Register ranges can be specified {r4, r5, r8-r10, fp, lr}
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers
x

## Slide 22: Preserving and Restoring Registers on the Stack Function entry and Function exit
Where {reg list} is a list of registers in numerically increasing order
example: push {r4-r10, fp, lr}
Registers cannot be: (1) duplicated in the list, nor be (2) listed out of numeric order
Register ranges can be specified {r4, r5, r8-r10, fp, lr}
Do not push/pop r12, r13, or r15
  the last two registers must always be fp , lr
Operation | Pseudo Instruction |  | Operation
Push registers Function Entry | push | {reg list} | sp = sp – 4 × #registers Copy registers to mem[sp]
Pop registers Function Exit | pop | {reg list} | Copy mem[sp] to registers, sp = sp + 4 × #registers
x

## Slide 23: push: Multiple Register Save (str to stack)
push copies the contents of the {reg list} to stack segment memory
push Also subtracts (# of registers saved) * (4 bytes) from the sp to allocate space on the stack
  sp = sp – (# registers_saved * 4)
this must always be true: sp % 8 == 0
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
save registers
push{r4-r6, r8, fp, lr}
r8
r4
r5
lr
fp
r6
CPU registers to Save
copy
Registers are pushed on to the stack in order
right (high memory) to left (low memory)
If you have no stack variables (later) then always push an EVEN number of registers!
sp after push
allocated space
(# registers) * (4 bytes)
stack segment low memory
stack segment high memory
x
sp before push

## Slide 24: pop: Multiple Register Restore (ldr from stack)
pop copies the contents of stack segment memory to the {reg list}
pop adds: (# of registers restored) * (4 bytes) to sp to deallocate space on the stack
  sp = sp + (# registers restored * 4)
Remember: {reg list} must be the same in both the push and the corresponding pop
stack segment high memory
r8
r4
r5
saved lr
saved fp
saved r8
saved r6
saved r4
saved r5
lr
fp
r6
stack segment low memory
CPU registers
copy
Restored register contents
Registers are pop’d from the stack in order
left (low memory) to right (high memory)
restore registers
pop{r4-r6,r8,fp,lr}
sp after pop
deallocated space
(# registers) * (4 bytes)
x
sp before pop

## Slide 25: Local Variables are Part of Each Stack Frame
Local variables are on the stack below the lowest numbered saved (pushed) register
#define BFSZ 4
int main(void)
{
char buf[BFSZ]; // BFSZ bytes
...
sp
saved lr
saved fp
buf[BFSZ]
BFSZ
buf[0]
buf[BFSZ-1]
x
saved register
saved register
sp
saved lr
saved fp
fp

## Slide 26: Stack Frame (Arm Arch32 Procedure Call Standards)
Stack Frame Requirements
Minimal frame: at function entry push {fp, lr}
sp points at top element in the stack (lowest byte address)
fp points at the lr copy stored in the current stack frame
Stack frames MUST ALWAYS BE aligned to 8-byte addresses
  So, this must always be true: sp % 8 == 0
x
Stack high address
low address
main
main's
frame
saved lr
saved fp
sp
fp
int main(void)
{
a();
/* other code */
return EXIT_SUCCESS;
}
int a(void)
{
int x;
int y;
/* other code */
return 0;
}
a
a's
frame
saved lr
saved fp
sp
fp
low address
saved lr
saved fp
sp
fp
minimal frame above
Always save at least fp and lr
and set fp at saved lr
allocate stack space
SP = SP – "space"
grows "down"
deallocate stack space
SP = SP + "space"
shrinks "up"
Function entry (Function Prologue):
  create frame (subtract
  save preserved registers
  allocate space for locals
  (subtracts from sp)
Function return (Function Epilogue):
  deallocate space for locals (adds to sp)
  restores preserved registers
  removes the frame
preserved registers
Local variables
sp
Note slide has builds
lr & fp must always be at top of frame

## Slide 27: FP_OFF: Distance from FP to SP Used to set FP at push and SP before pop
FP_OFF = (#regs - 1)*4 // -1 is lr offset from sp
Where # regs = #preserved + lr + fp
low memory
4-byte words
sp
saved lr
saved fp
saved r5
saved r4
after push {r4-r7,fp,lr}
add fp, sp, FP_OFF
fp = sp + 20 bytes
saved r7
saved r6
// other code etc .equ FP_OFF, 20
main:
push {r4-r7, fp, lr}
add fp, sp, FP_OFF …….
sub sp, fp, FP_OFF
pop {r4-r7, fp, lr}
bx lr
# regs saved | FP_OFF in Bytes
2 | 4
3 | 8
4 | 12
5 | 16
6 | 20
7 | 24
8 | 28
9 | 32
Function Prologue
always at top of function saves regs and sets fp
Function Epilogue
always at bottom of function restores regs including the sp
Function Stack Frame
FP_OFF:
Where to set FP after push
Means Caution, odd number of regs!
If odd number pushed, make sure frame is 8-byte aligned (later)
this must always be true: sp % 8 == 0
x
IMPORTANT: FP_OFF has two uses:
Where to set fp after prologue push (remember sp position)
Restore sp (deallocate locals) right before epilogue pop

## Slide 28: Function Prologue: Allocating the Stack Frame
saved fp
low memory
saved lr
sp
saved lr
saved fp
saved r5
saved r4
after
push {r4,r5,fp,lr}
saved fp
low memory
saved lr
sp
saved lr
saved fp
callers r5
callers r4
Set FP
add fp, sp, FP_OFF
fp
saved fp
low memory
saved lr
sp
at function entry
saved fp
low memory
saved lr
sp
Local Variables
Allocate Space for locals
ldr r3, =FRMADD
sub sp, sp, r3
saved lr
saved fp
saved r5
saved r4
FRMADD
x
fp
fp
Function was just called this how the stack looks
The orange blocks are part of the caller's stack frame
Function saves lr, fp using a push and only those preserved registers it wants to use on the stack
Function moves the fp to point at the saved lr as required by the Aarch32 spec
Allocate Space for Local Variables
fp
Part of function prologue
New Stack Frame
FP_OFF
FP_OFF

## Slide 29: Function Epilogue: Deallocating the Stack Frame
saved fp
low memory
saved lr
sp
Local Variables
At function exit after
pop {r4,r5,fp,lr}
saved lr
saved fp
saved r5
saved r4
Eligible for reuse
out of scope
x
At function exit (in the function epilogue) the function uses pop to restore the registers to the values they had at function entry
fp
Part of function prologue
saved fp
low memory
saved lr
sp
Local Variables
Stack frame while during function body execution
saved lr
saved fp
saved r5
saved r4
FRMADD
fp
FP_OFF
saved fp
low memory
saved lr
sp
Local Variables
Deallocate Space for locals
Put SP back so pop works
sub sp, fp, FP_OFF
saved lr
saved fp
saved r5
saved r4
Deallocated
Move SP back to where it was after the push so the pop works (this deallocates the local variables)
fp
FP_OFF
Use fp as a pointer to find local variables on the stack

## Slide 30: Local Variables on the Stack
Local variables are on the stack below the lowest numbered saved register
frame pointer is used as a pointer to stack variables
fp is the base register in ldr and str instructions
Example load buf[0] into r4
  FP_OFF = 12, BUFSZ = 4
  Distance from FP is buf[0] is 12 + 4 = 16
  ldrb r4, [fp, -16]
#define BFSZ 4
int main(void)
{
char buf[BFSZ]; // BFSZ bytes
...
sp
saved lr
saved fp
fp
buf[BFSZ]
BFSZ
FP_OFF
distance from fp to lowest saved register
buf[0]
buf[BFSZ-1]
BFSZ + FP_OFF
x
saved register
saved register
Calculate how much additional space is needed by local variables
After the register save push, Subtract from the sp the size of the variable in bytes (+ padding - later slides)

## Slide 31: Function prologue with local variables
move the sp to allocate space on the stack for local variables and outgoing parameters (later)
saved reg
saved reg
sp
fp
Stack after push
saved lr
saved fp
stack frame
x
push {fp, lr}
add fp, sp, FP_OFF
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
FP_OFF
FP_OFF
.equ FRMADD, 8
push {fp, lr}
add fp, sp, FP_OFF
ldr r3, =FRMADD // frames may be large sub sp, sp, r3
// your code
FRMADD
stack frame
size

## Slide 32: Function epilogue with local variables
For pop to restore the registers correctly:
  sp must point at the last saved preserved register put on the stack by the save register operation: the push
x
.equ FRMADD, 8
push {fp, lr}
add fp, sp, FP_OFF ldr r3, =FRMADD sub sp, sp, r3
// your code
sub sp, fp, FP_OFF
pop {fp, lr}
bx lr // func return
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
Return the sp (using the fp) to the same address it had after the push operation sub sp, fp, FP_OFF
this works no matter how much space was allocated in the prologue
FP_OFF
saved regs
saved regs
sp
local var
local var
fp
add space for local variables!
low memory
saved lr
saved fp
stack
frame
FP_OFF
FRMSZ
FRMSZ